## Slide 1: F5 Configuration document

## Slide 2: 1. F5 Integrated Solution 2.Setup Utility a. License Activation b. Management Settings 3. Network Configuration a. Vlan configuration b. Self IP configuration 4. Local Traffic a. Node configuration b. Pool configuration c. Virtual server configuration d. Profiles e. SSL Offloading e. iRule 5. System a. Configure NTP b. Configure SNMP c. Authentication using Remote Server 6. Packet Capture a. via CLI b. via GUI

## Slide 3: LTM Introduction
LTM delivers applications to users in a reliable, secure, and optimized way.
LTM is used to Load Balances the client request among the servers in a pool.
It uses multiple load balancing algorithm for distributing the client request.
LTM provides extensibility and flexibility of application services with the
programmability we need to manage your physical, virtual, and cloud
infrastructure.
It monitors the health & performance of the servers.

## Slide 4: F5’s Integrated Solution
The F5 Solution
Applications
Users
Mobile Phone
PDA
Laptop
Desktop
Co-location
CRM Database Siebel BEA Legacy .NET SAP PeopleSoft IBM ERP SFA Custom
TMOS
Application Delivery Network

## Slide 5: The Full Application Proxy
SYN
SYN ACK
ACK
Server Response
SYN
SYN ACK
ACK
Client Data
Client Data
TCP Express
Client Side Profile
Server Side Profile
Full Application Proxy – No More Relays
Internet

## Slide 6: Front Panel on most platforms
Sample device: BIG-IP 1600
Management Interface (10/100) - Default IP 192.168.1.245/24
2 USB Ports
Console Port
Default 19200/8/1/N
Hard-Wired Failover Port (blue outline)
Console cables and failover cable are pinned differently
10/100/1000 Copper Interfaces
Number varies based on platform
Gbics
Fiber interfaces, multi-mode (default) and single mode available, number varies by platform:
Type and Number depend on platform
Status LEDs
LCD and LCD Control Buttons
You can configure the management interface IP from the LCD

## Slide 7: Setup Utility

## Slide 8
BIG-IP web-based configuration
1. Access using default IP
2. License the BIG-IP
3. Run the Setup Utility
4. Configure BIG-IP objects( Nodes, Pools and Virtual Servers)
BIG-IP LTM Basic Configuration

## Slide 9
Use 192.168.225.128 or 192.168.1.245 default IP depending on the model
Click next for Setup Utility
Accessing LB For The First Time

## Slide 10: License Activation
Click on Next

## Slide 11
Copy the Dossier in Notepad

## Slide 12: Open https://activate.f5.com/license/dossier.jsp

## Slide 13
Paste the copied Dossier
Click on Next

## Slide 14
Click on next

## Slide 15
Copy the Licence

## Slide 16
Paste the copied Licence
Click on Next

## Slide 17
Device Rebooted Need Reconnection

## Slide 18
Click on Next
Licence Status

## Slide 19: Management Configuration
Configure MGMT IP, Mask, Gateway and Host name accordingly
Change CLI and GUI password
Enable SSH, Allow ssh for all IPs
Click Next

## Slide 20
After Click Next Click OK

## Slide 21
Access with new IP
Click to proceed

## Slide 22
Click Finished, as we want to configure advanced network setting
Now will jump from setup utility to configuration utility

## Slide 23: Configuration Utility
Vlan Configuration

## Slide 24
Click on Network

## Slide 25
Click on VLAN List

## Slide 26
Click to create vlan

## Slide 27
Type vlan name and vlan id
Interface can be tagged or untagged as per requirement
Click Finished

## Slide 28
Quick View on Configured Vlan

## Slide 29
Self IP and Floating IP Configuration

## Slide 30
Click on Self IPs

## Slide 31
Click create to configure self ip

## Slide 32
Name the self IP
Type IP address and mask as per requirement
Select vlan
Select non-floating as it is physical IP
Click repeat to configure floating

## Slide 33
Name the self IP
Type IP address and mask as per requirement
Select vlan
Select floating
Click to finish

## Slide 34
Quick View on Configured IPs

## Slide 35: Node Definition

## Slide 36
Web Nodes
TXN Nodes
Web 1 192.168.21.4
Web 2 192.168.21.5
Web 2 192.168.21.6
TXN 1 192.168.21.7
TXN 2 192.168.21.8
TXN 3 192.168.21.9
TXN 4 192.168.21.10
Gateway
F5
Node-: A node is a logical object on the BIG-IP® system that identifies the IP address of a physical resource on the network.

## Slide 37
How to configure Node

## Slide 38
Click on Local Traffic
Click on Node list

## Slide 39
Click on Create
Type Name, Node IP and leave rest of the details default
Click to Finish

## Slide 40
Similarly Create another node
Quick View on Configured interfaces

## Slide 41
Pool Definition

## Slide 42
Web application pool
TXN application pool
Web 1 192.168.21.4 :9990
Web 2 192.168.21.5:9999
Web 2 192.168.21.6:9999
TXN 1 192.168.21.7:9898
TXN 2 192.168.21.8:9898
TXN 3 192.168.21.9:9898
TXN 4 192.168.21.10:9898
Gateway
F5
Application 1
Application 2
Pool:- A load balancing pool is a logical set of devices, such as web servers, that you group together to receive and process traffic.

## Slide 43: How to configure Pool

## Slide 44
Click on Pool List
Click to create Pool

## Slide 45
Type name and select health monitor according to requirement
1. Select node from node list 2. Fill service port 3. Click on to add
Click on Finish

## Slide 46
Quick View on Configured Pools

## Slide 47: Virtual Server Definition
A virtual server is a traffic-management object on the BIG-IP system that is represented by an IP address and a service. Clients on an external network can send application traffic to a virtual server, which then directs the traffic according to your configuration instructions. The main purpose of a virtual server is often to balance traffic load across a pool of servers on an internal network. Virtual servers increase the availability of resources for processing client requests

## Slide 48
Web application pool
TXN application pool
Web 1 192.168.21.4 :9990
Web 2 192.168.21.5:9999
Web 2 192.168.21.6:9999
TXN 1 192.168.21.7:9898
TXN 2 192.168.21.8:9898
TXN 3 192.168.21.9:9898
TXN 4 192.168.21.10:9898
Gateway
F5
Application 1
Application 2
VIP 192.168.21.11 :9999
VIP 192.168.21.11 :9898
Users

## Slide 49: Configure Virtual Server

## Slide 50
Click on Virtual Server List
Click on Create

## Slide 51
To be continued
Type name of virtual server
Type VIP IP and service port(listening port)
Leave other setting default

## Slide 52
Select Auto map from dropdown
Select Pool that need to load balanced
Click to finish

## Slide 53
Session Persistence
Goto Virtual Server  Resources tab
Choose Persistence Profile

## Slide 54
Quick View on Configured Virtual Servers

## Slide 55: Profiles Definition
Profiles are a configuration tool that you can use to affect the behaviour of certain types of network traffic. More specifically, a profile is an object that contains settings with values, for controlling the behaviour of a particular type of network traffic, such as HTTP connections. Profiles also provide a way for you to enable connection and session persistence, and to manage client application authentication.

## Slide 56
How to Configure Profiles

## Slide 57
Click on HTTP
Click to Create for new Profile

## Slide 58
Name the profile
Select parent profile http
Select custom
To be continued
Select Insert X-Forwarded-For Enabled

## Slide 59
Click on Finished

## Slide 60
Attach Profile to Test-VS
Select profile
Click on Update

## Slide 61
SSL Offloading
    It is a feature of F5 in which request from client to f5 in encrypted (i.e HTTPS) then F5 offload the SSL data from
    HTTPS request & then forward the client request to Server in HTTP format.
    After that Server response back in HTTP to F5 then F5 encrypt response to HTTPS format & send to client
    So in this way Servers Resources are saved that were previously used in SSL (Handshaking, encryption, Decryption) & in this way server performance Increases.
    According to a research Server Takes 10 times the time to process HTTPS request as compare to the HTTP Request.
    Requirement
    Before we configure it we must have SSL certificates & Key for our Website.
    There are Two Method for Creating Certificates & Key
    1. Self signed by F5 Device 2. By Certificate Authority

## Slide 62
Generating Self Signed Certificates
Self signed by F5 Device
Go to System File Management
 SSL_Certificate_List then create new.
Now add the information as shown
In diagram.
So we have created self-signed SSL
Certificates & Key.
Now we will create a Client SSL Profile.

## Slide 63
CA Certificates
2.Add Certificates Provided by CA
Go to System File Management
 SSL_Certificate_List Import
Now select Import type as Certificate.
Give a name to it.
Browse the Certificates Provided by CA.
Then Click import.

## Slide 64
Import Key to F5
Add Key Provided by CA
Go to System File Management
 SSL_Certificate_List Import
Now select Import type as Key.
Give a name to it.
Browse the Key Provided by CA.
Then Click import.

## Slide 65
Client SSL Profile
Open the Local Traffic > Profiles > SSL > Client page, and then click Create
Now fill the required information as shown. Click Custom then Add for Certificate Key Chain then select Certificate & key we created & click Finished.

## Slide 66
Go to Local Traffic Virtual Servers & select the virtual server.
Now assign the Client SSL profile that we created to Virtual Server in the configuration field & click update at bottom.
Now when client make HTTPS request to this VS ip then F5 will offload SSL & will send request in HTTP to node.
In response F5 will encrypt the response to HTTPS & will forward to client.

## Slide 67: iRULES
An iRule, in its most simple terminology, is a script that executes against network traffic passing through an F5 device
iRules can route, re-route, redirect, inspect, modify, delay, discard or reject, log or do just about anything else with network traffic passing through a BIG-IP
iRule allows us to use the advance feature of F5 which we can’t use via CLI or GUI

## Slide 68
Click on iRule list
Click on Create

## Slide 69
Paste the iRule
Click on Finish

## Slide 70: Attach iRule to Virtual Server
Click on Test-VS
Click on Virtual Server

## Slide 71
Click on Resources
Click on Manage

## Slide 72
Select Test-iRule
Click on Finished

## Slide 73: Authentication using Remote Server
We will use tacacs+ for authenticating user traffic
Goto System  Users  Authentication
Fill the following details

## Slide 74: Authentication using Remote Server
Assigning access control properties to user groups
Goto System  Users  Remote Role Groups
Click create
Fill the following details

## Slide 75
NTP Configuration

## Slide 76
Click on NTP
Add NTP IP
Click for Update

## Slide 77: SNMP Configuration

## Slide 78
Insert SNMP server IP and Add
Click on Configuration
Click to Update

## Slide 79
Select SNMP version According to requirement
Click on Create

## Slide 81: Packet Capturing on F5 LB

## Slide 82
Capturing Packets from CLI
Packet Capture from Command Line on F5 LB-
  Use the command tcpdump –D to see all available interfaces.
To See list of all available Interfaces
We selected interface no. 1 i.e eth0
Tcpdump try to resolve IP to Name from DNS

## Slide 83
Use the command tcpdump –h for Help.
-n used to stop IP to name resolution
Filter traffic to/from host 10.1.1.1

## Slide 84
Using IP, Port based filters-
Filtering packets on Port 22
Packets only form source 10.1.1.1

## Slide 85
TCP Flags based filters-
Packets with ACK & RESET flags only
Packets with only ACK flag set

## Slide 86
Using Combined Filters-
Only Packets that match src 10.1.1.1 & flag push as set

## Slide 87
Using Combined Filters-
Only Packets matching dst IP 10.1.1.1, src port 23 & tcp flag reset

## Slide 88
Stop Capture after 5 packets
Saving Packet Captured from Host 10.1.1.1 to a test.pcap file

## Slide 89
Capturing Packets via GUI
Goto System  Support, then tick TCP Dump box. Select VLAN, No. of packets to Capture. Apply filter in options field.
Then Click Add. Select Timeout & click Start

## Slide 90
Now Download the Snapshot File. The file will be downloaded as .tar.gz, now extract this file.
We will find a file with .dmp extension, now rename it as .pcap so we can analyze it in wireshark.

## Slide 91
Copy Capture File from Server to PC
As we have save the captured packets to a file on server, now we will copy this file from server to our pc on which
Wireshark is installed to analyze the packets.
We will use WinSCP App to achieve this. First open the WinSCP app that is installed on our pc. After that it will ask to login, type IP or Hostname in Hostname field, Port no., Username & Password & click login.
Remember to copy file from server we must have connectivity to the server.

## Slide 92
Now we will get a Window as shown below. On left side is our PC & on Right side is Server Directories.

## Slide 93
Now drag & drop the captured file from server directory to our PC.
Now we have the captured file on our pc & we can analyze it using Wireshark GUI.

## Slide 94
Thank You